## Slide 1
IoT Node CA Registration
Connect 2 Azure
Secure connectivity using OPTIGA™ Trust M
IoT Node Provisioning
Microsoft
Azure
IoT Node Controller
Application
MQTT Service
TLS Stack
OPTIGA™ Library
Toolbox Commands
Gen Random
Hash (SHA256)
Generate Key Pair (ECC, RSA)
Sign (ECDSA, RSA)
Verify Signature
(ECDSA, RSA)
Encrypt/Decrypt (RSA)
Key Derivation (ECDH, TLS 1.2 PRF)
Storage Commands
Read Data Object
Write Data Object
Protected Update of Data
Secure Storage
Key Objects (E.g. RSA and ECC)
Data Objects (E.g. Trust Anchors, Certificates, Pre-shared secrets, Counters and etc.)
TLS Stack
MQTT Service
Shielded Connection
Over I2C
IoT Node with
OPTIGA™ Trust M
TCP/IP
Communication
IoT Node Controller and OPTIGA™ Integration overview
Demo Setup
IoT Node CA
Certificate
Microsoft Azure
MQTT: Publish
Messages
MQTT: Subscribe
Messages
OPTIGA™ Trust M
ESP32 with
OPTIGA™ Trust M
IoT Node
Monitor: Device Management tool
Secure connectivity using OPTIGA™
Establishes a Secure Connection to Microsoft Azure cloud using OPTIGA™ Trust M
OPTIGA™ Trust M is a hardware security module (CC EAL 6+ certified hardware)
  Performs the cryptographic operations during the TLS handshake.
  Secure storage for private key(s) used for the client / node authentication.
  Secure storage for device certificates and cloud server Trust Anchors.